## Slide 1: Yield Modeling with EXOSIMS for HabEx
Dr. Rhonda Morgan
Jet Propulsion Laboratory, California Institute of Technology
June 13, 2016
© 2016 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: What is EXOSIMS? https://github/dsavransky/EXOSIMS
EXOSIMS is a yield software architecture in which every model component can be independently upgraded/changed.
  A Monte Carlo approach allows for dynamic constraints in the scheduling of the design reference mission (DRM), such as star shade fuel consumption and responses to detections.
  Creates ensembles of DRMs which can be analyzed statistically.
✖
✔
✖
✔
✖
✔
✖
✖
✔
2 Detections
1 Detection
1 Detection

## Slide 3: A Single DRM run
EXOSIMS keeps track of time and lists the start time of a new observation. For this demo run the mission lasted 36 days.
  The observing time was dominated by the 1 day optical overhead time.

## Slide 4: Single DRM output
EXOSIMS does not (yet) automatically write out the data and generate analysis graphs for the user.
The results of the run and all parameters are stored as python objects (mix of arrays, dictionaries, lists , etc.)
1st star visited
Detection integration time (days).
Detection status:
0 = null detection
1 = detection
-2 = false alarm
-1 = missed detection
Index of star used in target list (TargetList.Name)
Index of planet In list of synthetic planets

## Slide 5: Ensemble of DRMs Output
The ensemble output is a list of DRMS:
    Sim.SurveySimulation.DRM[:]
Illustrative Output
Still Debugging Results

## Slide 6: Initial Ensemble Runs Performed
The first set of ensemble DRMs were run using parallel processing on a 48 core server.
  In progress is running parallel over ssh to a potential 131 cores.
The runs are in the shake down phase. Debugging is in process.
Dmitry Savransky is working to increase code speed
Larger target lists result in longer run times
Diam m | Mission yrs | Char. lambda | Num. DRMs | Machine | Num. threads | Runtime hrs
4 | 3 | 1 um | 80 | aftac3 | 40 | 8
4 | 3 | 400 nm | 80 | aftac3 | 40 | 14.4
8 | 6 | 1 um | 100 | aftac3 | 40 | 82
8 | 3 | 400 nm | 80 | aftac3 | 40 | 44

## Slide 7: Inputs
https://docs.google.com/spreadsheets/d/1-w1eybYV6nyX02kH7eoNWie8UinzlVnLM4F-64AagHw

## Slide 8: Yield study goals
Yield modeling of key point designs and trades
The first study is sensitivity to aperture diameter
We also want to look at
  Coronagraph only
  Coronagraph + star shade hybrid
  Star shade + star shade + star shade + …

## Slide 9: How do we know the code is right?
Validate against other codes
  Many options exist: Stark, Traub, Nemati
  A good top level comparison of results at the finish line
  Compares Monte Carlo outputs on complex codes
  Many assumptions (~100) in yield code drive the results
Point-check the physics
  A good grassroots, bottom up approach
  Done in smallest chunks of code sensible (unit tests)
  Each test is tailored to that unit of code
    Some test software things
    Some test physics results against expected values

## Slide 10: Brown Completeness Cloud Unit Test Qualitative Example
Brown 10^8 samples
10^5 samples in ExYM
10^5 samples in EXOSIMS
BrownCompleteness
I scaled this axis to match Brown
The y-axis is incorrect due to a discovered unit mismatch (km to AU)
This case duplicates Brown’s values for verification

## Slide 11: Test Case for Cp, Cb, Tint
Use Known RV planets from IPAC portal
Validated Matlab code computes photon counts from planet and background and detector noise sources and calculates integration time

## Slide 12: Choose missing data to design for a good software test
We verified that a range of planet radii were represented. Planet radius was calculated from planet mass (from IPAC).
A variety of inclinations and phase anomalies were chosen to span the parameter space

## Slide 13: How much code has been tested?
We have written 2714 lines of test code for 134 functions.
Test code will be delivered to github and can be used for regression testing.

## Slide 14: Remaining Testing
Unit Tests
  Resolve Integration Time Discrepancies
  Validate KeepOut window
  Hand Trace scheduler decisions
End to End Testing
  Shakedown of initial ensemble runs
  Cross validation with Chris Stark’s AYO code is planned for FY17 under the Standard Definitions and Evaluation Team

## Slide 15: Anticipated Output Products
Mission Failure Modes
False Alarm Probability varies with separation
Instrument Bias
Mission Execution
Savransky and Garret, 2015

## Slide 16: backup

## Slide 17: Simulated Mission Ensemble
Simulate a universe by sampling planet population distributions
Schedule a mission using spacecraft and mission observing constraints
  Dynamically respond to detections
Repeat with a new universe 1,000 times
Detect
Schedule
Missionj
Yield
Stats
Simulate Universej
(populate planets)
Monte Carlo DRMs (Design Reference Missions)
Planet Populations
Characterize
Star
Catalog
Instrument

## Slide 18: EXOSIMS Architecture
D. Savransky, 2016
EXOCAT1
BrownCompleteness
EarthTwinHabZone1
EarthTwinHabZone2
KeplerLike1
FortneyMarleyCahoyMix1
KeplerLikeUniverse
WFIRSTObservatoryL2
Nemati
GalaxiesFaintStars
Stark
Discovery of synthetic planets
HabZoneExoearthUniverse
KasdinBraems

## Slide 19: EXOSIMS Architecture
D. Savransky, 2016
KnownRVPlanets
KnownRVPlanetsUniverse
WFIRSTObservatoryL2
Nemati
GalaxiesFaintStars
Stark
Characterization of Known planets
KnownRVPlanetsTargetList
KasdinBraems

## Slide 20: Draft Input Parameter Request
ExEP Yield Input Parameters |  |  | 
 | Input | Default | Notes
Astrophysics |  |  | 
type of planets |  | EarthTwin | uniform random, keplerLike, KnownRV
EarthTwin |  |  | 
eta_earth |  | 0.16 | 
planet radius |  | 1 earth radius | 
planet mass |  | 1 earth mass | 
geometric albedo |  | 0.2 | Lambert phase function is used
semi-major axis |  | [0.75, 1.5] AU | uniform random distribution
eccentricity |  | [0,0.35] | uniform random distribution
cos(inclination) |  | [-1, 1] | uniform random distribution
argument of perigree |  | [0, 360] degrees | uniform random distribution
ascension of the ascending node |  | [0, 360] degrees | uniform random distribution
Zodical Light model |  | Stark | local zodi, interpolates for longitude
exozodi mean and variance |  | 22 mag/asec^2 | no spatial variance. Variance is log normal star to star.
Telescope |  |  | 
Diameter of pupil | study parm |  | 
shape factor |  | pi/4 | shapeFac * D^2 = Area
obscuration factor |  | 0.2 | due to spiders, secondary
throughput |  | 0.57 | Telescope only, not coronagraph
telescope keep out angle |  | 45 degrees | sun avoidance
Detection lambda |  | 550 nm | 
detection bandwidth |  | 0.2 | delta_lambda/lambda
Spectra central lambda |  | 550 nm | 
spectral BW |  | R 70 | 
SNR detection |  | 5 | 
SNR characterization |  | 10 | 
limiting deltamagnitude |  | 26 | 
minimum completeness |  | 0.1 | 
integration time cutoff |  | 30 days | maximum allowed integration time
Occulters |  |  | 
Internal Coronagraph type |  | HLC | 
IWA |  | 2.5 lambda/D | 
OWA |  | 10 lambda/D | 
Contrast |  |  | 
Throughput for Coronagraph |  |  | 
delta_mag limit |  | 26 | 
DetectionTimeMultiplier |  | 1 | 2 for polarizations, another 2 for RDI
CharacterizationTime Multiplier |  | 1 | 2 for polarizations
Optical Overhead time |  | 1 day | 
starshade diameter tip to tip |  |  | 
number of starshade distances |  |  | 
starshade distance |  |  | km
starshade blue edge |  |  | nm
starshade red edge |  |  | nm
Detectors |  |  | 
imaging or spectrometer |  |  | 
dark current |  | 0.00009 e-/s | defaults are for WFIRST EM-CCD
readNoise |  | 3 e- | 
exposure time per frame |  | 1000 seconds | 
QE |  | 0.88 | 
R |  | 70 | 
CIC |  | 0.0013 | 
ENF |  | 1.414 | sqrt(2)
EM CCd gain |  | 500 | 
Post Processing |  |  | 
post-processing contrast factor |  | 1/10 | input can be [0,1]. 1/10 and 1/30 are common
allowable false alarm probability |  | 3.00E-05 | 
allowable missed detction probability |  | 1.00E-03 | 
Mission |  |  | 
mission lifetime |  | 5 years | 
fraction to exoplanets |  | 0.5 | 
start date |  | January 1, 2036 | 
Observatory |  |  | 
settlingTime |  | 1 day | after repointing, especially for occulter formation flying
occulter slew thrust |  | 450 mN | 
occulter slew Isp |  | 4160 | specific impulse
occulter initial wet mass |  | 6000 kg | 
Telescope spacecraft mass |  | 5800 kg | 
occulter station keeping Isp |  | 220 | specific impulse
default burn portion for slew |  | 0.05 |