## Slide 1
Next-generation Thermopile Detector Array for Far-Infrared Space-Based Remote Sensing
National Aeronautics and Space Administration
Postdoc Research
National Aeronautics and Space Administration
Jet Propulsion Laboratory
California Institute of Technology
Pasadena, California
www.nasa.gov
Clearance Number: CL#00-0000
Poster Number: Postdoc-T-006
Copyright 2025. All rights reserved.
Publications and Acknowledgements:
Eom, B. H., Pepper, B., Braga Nogueira Branco, R., Greenhagen, B. T., & Kenyon, M. E. (2025). Development of a next-generation thermopile detector for cold-body space applications. IEEE Sensors Journal, 1–9. https://doi.org/10.1109/JSEN.2025.3595487
Braga Nogueira Branco, R., H. Eom, B., Pepper, B., & E. Kenyon, M. (2025). Fabrication of Cantilever Absorber Structures for Enhanced Performance of Space-Based Far-Infrared Thermopile Detectors. 2025 50th International Conference on Infrared, Millimeter, and Terahertz Waves (IRMMW-THz).
Braga Nogueira Branco, R., H. Eom, B., Pepper, B., & E. Kenyon, M. (2025). Development of a high-fill-factor thermopile array for space-borne far-infrared radiometry. 2025 SPIE Sensors + Imaging Conference.
Braga Nogueira Branco, R., H. Eom, B., Pepper, B., & E. Kenyon, M. (2026). Progress Towards a Near-Unity Fill Factor FIR Thermopile Detector for Space-Based Remote Sensing. 2026 IEEE Aerospace Conference (Under review)
Author Contact Information: rbranco@jpl.nasa.gov
Background
High-priority science questions can be answered by exploring the far-infrared (FIR) spectrum
Thermopile detectors are uncooled thermal detectors that can perform remote-sensing (thermal imaging, spectroscopy, and energy balance) throughout the Solar System, including primitive bodies, planets, and satellites.
Key capabilities of thermopile detectors:
Broadband (0.3 to >200 m), covering full range of albedo and thermal emission.
Broad temperature range operation (>200 to <350 K).
Insensitive to instrument temperature drifts.
Negligible excess 1/f noise (long integration times).
Highly linear to incident radiation (50x more than microbolometers).
Goal
128x64 pixels
97% fill factor
State-of-the-art (PREFIRE)
64x8 pixels
~ 25% fill factor
Design a new detector architecture that accommodates 8,192 pixels with individual wiring connections
Develop a process to fabricate a stacked, two-layer, wiring bus to minimize the spacing between pixel rows.
Develop a process to fabricate large three dimensional ‘cantilever’ absorber structures, where the wiring and pixels sit underneath.
Fabricate and test a complete 128x64 array with the multi-tiered wiring and ‘cantilever’ absorbers.
Objectives
Approach and Results
Significance of Results/Benefits to NASA/JPL
Future Work
=
FIR science throughout the Solar System: Uranus, Earth, Moon, primitive bodies, etc.
Will enable high spatial resolution thermal imager with hyperspectral capability within a small cost, size, and weight (c-SWaP) package.
Klayout software to create the design and Python script to generate parametric wiring connections.
Deposit silicon nitride as the interlayer dielectric between wire layers and develop a process to liftoff rows of pixels for subsequent patterning.
Deposit polyimide as a sacrificial layer, pattern the structure shape, deposit silicon nitride as the absorber structure, and etch the polyimide underneath.
Use knowledge obtained from Objectives 1-3 to update design, fabricate a full 128x64 pixel array, and test the responsivity under vacuum.
1
2
3
4
1
2
3
4
1 mm
Wiring
ROIC output
Pixels
Complete Objectives 3 and 4 by fabricating large absorber structures with fully removed sacrificial layer and fabricating and testing a 128x64 pixel array.
Share progress through conference presentations and publications.
3
4
Wire layer 2
340 nm
Wire layer 1
180
180
Wiring
Suspended Thermoelectrics
Absorber
Absorber
100 m
2
1
Thermal map from PREFIRE
Learn more about PREFIRE
Learn more about Diviner
Thermal map from JPL’s Diviner on LRO
The Uranus Orbiter and Probe mission concept calls for a Diviner-like instrument
Image adapted from: “PLANETARY MISSION CONCEPT STUDY FOR THE 2023–2032 DECADAL SURVEY - Journey to an Ice Giant System – Uranus Orbiter and Probe”, 7 Jun 2021, https://science.nasa.gov/wp-content/uploads/2023/10/uranus-orbiter-and-probe.pdf
FIG 1: Spectral radiance of cold space bodies peak in the FIR.
FIG 2: A FIR thermopile detector can perform thermal imaging and spectroscopy of the Earth, Moon, Uranus, and other bodies in the Solar System.
Incident Power, P
T1
n-type: S2
p-type: S1
Active Layer
T2
Reference Layer
Detector Sensitivity
G is thermal link between T1 & T2
A: Pixel area Noise Responsivity
FIG 3: A voltage is induced across a series of N couples proportional to the Seebeck coefficient and
FIG 4: The next-generation detector architecture (Right) will have a larger format size, diffraction-limited pixels, and near unity fill factor when compared to the detector used in PREFIRE (Left).
FIG 5: Results corresponding to Objectives 1-3.
3
Author: Ricardo Braga Nogueira Branco (389I, NASA Postdoctoral Fellow)
Matthew E. Kenyon (389I)
Thermopiles work by converting a temperature gradient to a voltage through the Seebeck effect.
100 m