## Slide 1
National Aeronautics and Space Administration
Jet Propulsion Laboratory
California Institute of Technology
Pasadena, California
www.nasa.gov
National Aeronautics and Space Administration
Novel Heterodyne Detectors for THz High-resolution Spectroscopy
Author: Changyun (Chang) Yoo, NASA Postdoctoral Fellow (386H)
Supervisor: Boris Karasik (386H)
Collaborators: Jonathan Kawamura (386H), Chris Curwen (386H), Changsub Kim (389I), Daniel Cunnane (389I), Mark Sherwin (UCSB)
Postdoc Research
Clearance Number: CL#00-0000
Poster Number: PRD-T-001
Copyright 2023. All rights reserved.
Publications:
D. Cunnane et al., "Optimization of Parameters of MgB2 Hot-Electron Bolometers," IEEE Transactions on Applied Superconductivity, vol. 27, no. 4, pp. 1-5, 2017
C. Yoo et al., "Demonstration of a tunable antenna-coupled intersubband terahertz (TACIT) mixer," Applied Physics Letters, vol. 116, no. 1, 2020
Author Contact Information:
chang.yoo@jpl.nasa.gov
Path Forward
Hot-Electron Bolometer (HEB) Mixer Based on High-Tc Superconductor
Tunable Antenna-Coupled Intersubband Terahertz (TACIT) Mixer
THz Heterodyne Spectrometer
THz Signal
THz Local-Oscillator (LO)
Low
Back-end
Spectrometer
Heterodyne Detector
(Mixer)
Low-noise Amplifier
Room-T Amplifiers
Cooled to cryogenic temperature
Motivation
The motivation for this work comes from the continuous and ongoing need for sensitive THz mixers at 1 - 5 THz that operate at a high operating temperature (> 20K) with a wide intermediate-frequency (IF) bandwidth (>10 GHz) and a small required local-oscillator (LO) power (< 1 µW).
THz RF, LO
GHz IF
Top Gate
Bottom Gate
Source
Drain
TACIT mixer is based on a single, 40-nm wide GaAs/AlGaAs square quantum-well (QW) heterostructures.
THz absorption occurs via tunable quantum transitions (intersubband transitions), and the IF signal is read out by the hot-electron bolometric response of the 2-dimensional electron gas (2DEG).
The detection frequency can be tuned in a wide range (2 -5 THz) with electrostatic biases, and a wide IF bandwidth (~ 10 GHz) is possible thanks to the fast energy relaxation (τ ~ 10 ps) in the 2DEG.
MgB2 mixers are based on thin (< 20 nm) MgB2 superconducting films that have high Tc (~ 40 K for bulk).
In MgB2 HEB mixers, THz absorption occurs via Joule heating, and the IF response comes from the bolometric response due to the electron heating.
Fast energy relaxation in MgB2 thin films offers wide (~ 10 GHz) IF bandwidth.
Mixer Technology | DSB Noise Temperature | Operating Temperature | Required Pump (LO) Power | IF Bandwidth
Superconducting HEB (MgB2) | < 2,000 K | > 20 K | ~ 1 µW | ~ 10 GHz
TACIT | < 2,000 K | 20 – 60 K | ~ 1 µW | ~ 10 GHz
Science Objectives
High-resolution (f/Δf > 107) spectroscopy at THz frequencies (1-5 THz)
Detection of key molecules and atoms in the interstellar space and in the atmospheres of planets and comets
Study of kinematics of THz emitting bodies and wind velocities
High-resolution spectroscopy at THz frequencies is enabled by heterodyne detection.
Past & Future THz Heterodyne Instruments
Herschel Space Observatory
HIFI: 0.48 - 1.25 THz
1.41 - 1.91 THz
SOPHIA
GREAT: 1.4 - 1.9 THz, 2.4 - 2.7 THz, and 4.7 THz
STO-2 and ASTHROS
1.4 - 1.5 THz; 2.4 - 2.7 THz
JUICE
SWI: 530 - 625 GHz; 1080 - 1275 GHz
MIRO: 190, 562 GHz
Rosetta Orbiter
AURA
MLS: 118, 190, 240, 640, 2500 GHz
Our mixer technology based on MgB2 HEBs and TACIT mixers will enable sensitive, multi-pixel THz heterodyne receivers with relaxed requirements on cryogenic cooling and THz LO power.